Data Structures

Data Structures

- Data structures is a particular way of organizing data so that it can be used efficiently.
- Data structures can implement one or more particular abstract data type ADT), which specify the operations that can be performed on a data structure and the computational complexity of those operations.
Abstract Data Type (ADT)

- ADT is a set of elements with a collection of well defined operations.
- Examples: List, Stack, Queue, Tree etc.

Complexity of Algorithms

Complexity of a algorithm is a rough estimation of the number of steps performed by given computation depending on the size of the input data.
1. Time compexity : Running time of the program as a function of the size of input.
2. Space complexity : Amount of computer memory required during the program execution, as a function of the input size.

Big O notation : A convenient way of describing the growth rate of a function.	(Time complexity)

- O(1) : Refers to constant time.
- O(n) : Indicates linear time.
- O(n pow k) : Refers to polynomial time.(k is fixed)
- O(log n) : Indicates logarithamic time.
- O(2 pow n) : Refers to exponential time.etc.

Best Case : An upper bound on the running time for any input of given size.

Average Case : Assume all inputs of a given size are equally likely.

Worst case : The lower bound on the running

Lists

- A list also called a sequence, is a container that stores elements in a certain linear order which is imposed by the operations performed.
- The basic operations supported are retriving, inserting and removing an element given its position.
- The basic realization of sequence is by means of arrays and linked lists.

Linked Lists

Linked list is a linear collection of data elements, called nodes pointing to the next	node by means of a pointer.

1. Single Linked List : Single linked list contain nodes which have a data part as well as an address part which point to the next node.
2. Doubly Linked List : In a doubly linked list, each node contains two links the first link points to previous node and the next link points to the next node in the sequence.
3. Circular Linked List : In the circular linked list the last node of the list contain the address of the first node and forms a circular chain.

Stack

- Stack is a special kind of list in which all insertion and deletions occur at one end , called the end.
- Stack is ADT is a special case of the list ADT it is also called as LIFO list or pushdown list.
- Typical operations : retrive, push, pop.
- Application : undo button.

Queue

- A queue is a special kind of a list in which all items are inserted at one end (called rear end) and deleted at the other end (called the front end).
- It is also called as FIFO.
- Typical operations : retrive, enqueue, dequeue.
- Application : printer.

Tree

- A tree is a widely used abstract data type that simulates a hieraachical tree structure, with a root value and subtree of children with a parent.
- Node : Each element of tree is called a node.
- Edges : The lines connecting the nodes are called edges or branches.
- Pareent Node : The immediate predecessor of a node is called parent node.
- Child Node : All immediate successors of a node are its child nodes.
- Root Node : This is specially designated node that does not have any parent.
- Leaf Node : A node that does not have any child is called leaf node or terminal node.
- Level : Level of any node is defined as the distance of that node from the root.
- Height : The total number of levels in a tree is the height of the tree.
- Siblings : Two or more nodes which have same parent are called siblings.
- Path : Path of a node is defined as a sequence of nodes N1, N2...Nm such that each node Ni is parent of N i+1, for 1 < i <m. In a tree there is only one path between twi nodes.
- Ancestor and Descendent : If there is a path from node a to node b then, a is called an ancestor of b and b is called a descendent of a.
- Subtree : A subtree of a tree is a node in that tree together with all its descendents.
- Depth : The depth of a node is the length of the unique path from the root to the node.

Tree Traversal

- This is a systematic way of ordering the nodes of a tree. Threre are some schemes for tree traversal :
  - Preorder : NLR
  - Inorder : LNR
  - Postorder : LRN
  - Level order : Nodes are visited from top to bottom and from left to right.

Binary Tree

- A binary tree is either empty or consists of a node called the root together with two binary trees called the left subtree and right subtree.
- Typical operations : traversal, insert and delete.

Strictly Binay Tree

A binary tree is strictly binary tree if each node in the tree is either a lesf node or has exactly two children i.e. there is no node with one child.

Full Binary Tree

A binary tree is full binary tree if all the levels have maximum number of nodes.

AVL Tree

- Adelson, Velski and Landis , AVL tree are height balancing binary search tree.
- AVL tree checks the height of left and right subtree and assumes that the difference is not more than 1. The diffrence is called balancing factor.
- AVL Rotations : To make itself balanced, an AVL tree may perform four kinds of operations.
1. Left Rotation.
2. Right Rotation.
3. Left-Right Rotation.
4. Right-Left Rotation.
Red Black Tree

- Red black tree is balanced binary tree in which every node is colored either red or black.
- Null links are replaced by special nodes that are called external node.
- Properties of RB Tree :
  - Root is always black.
  - All external nodes are black.
  - A red node can not have red children, it can have only black children.
  - There is no restrictionon on the color of the children of a black node i.e. black node can have red or black children.
  - For each node N, all paths from node N to external nodes contain the same number of black nodes. This is called black height of that node.
- Grandparent : Grandparent of a node is the parent of the parent node.
- Sibling : Sibling of a node is the other child of parent node.
- Uncle : Uncle is sibling of parent node.
- Nephews : Nephews of a node are the children of the sibling node.
- Near Nephew and Far Nephew : If node is left chils, then left child of sibling node is near nephew and if node is right child, then right child of sibling node is near nephew otherwise it called as far nephew.

Sorting

- Sorting refers to arranging the data according to their values in some specified order where order can be either ascending or descending.
- In – Place Sorting : In – place sorting methos generally use the same storage that is occupied bt input data to store the output data while sorting.
- Not In – Place Sorting : Not In – Place sorting algorithm may need extra storage to store intermediate results of the sorting and at last sorted data copied back to original storage.
- Selection Sort
    - Search the smallest element from array.
    - Exchange this element with first element of an array.
    - Search the smallest element from second element and replace it with second element of an array.
    - Repeat the above steps for all element and the result will be sorted array.
    - Time complexity is O(n*n)
- Bubble Sort
    - Compare arr[0] and arr[1], if arr[0] > arr[1] then exchange.
    - Compare arr[1] and arr[2], if arr[1] > arr[2] then exchange.
    - Repeat the process for all elements.
    - In the first iteration largest element is placed at last position of array.
    - If data is sorted order time complexity is O(n) and if data is reverse or random order time complexity is O(n pow 2).

- Insertion Sort
    - The insertion sort proceeds by inserting each element at the proper place in sorted list.
    - The array is searched sequebtially and unsorted items are moved and inserted into sublist .(int the same array)
    - If list is almost sorted then time complexity is O(n) and list is not sorted then time complexity is O(n pow 2).

- Merge Sort
    - Merge sort is sorting technique based on devide and conquer technique.
    - Merge sort first devides the array into equal halves and then combines them in a sorted manner.
    - Time complexity is O(nlogn).
- Quick Sort
    - Quick sort is a heighly effiecient sorting algorithm and is based on partitioning of array of data into smaller array.
    - A large array is partitioned into two arrays one of which holds values smaller than specified value say pivot , based on which the partition is made and another array hold values greater than pivot value.
    - After partitions an array quick sort calls itself recursively twice to sort the resulting subarray.
    - Time complexity is O(nlogn)

Searching

- Linear Search
  - In this searching technique, a sequential seach is made over all items one by one.
  - Every item is checked and if match found then that particular item is returned otherwise search continues till the end of the data collection.
- Binary Search
  - Binary search is fast search algorithm with runtime complexity O(log n).
  - This search algorithm works on the principle of devide and conquer technique.
  - For this algorithm data should be in a sorted order.
  - Binary search, search a particular item by comapring the middle most item of the collection.
  - If match occurs then index of item is returned.
  - If middle item is greater than item then item is searched in sub list to the right of mddle item otherwise item is search in sub list to the left of the middle item.
  - This process continues on sub list as well as untill size of sublist reduces to zero.